## Slide 1: Adaptive Pilot Placement for OFDM Channel Estimation
GRADUATE RESEARCH REVIEW
Data subcarrier
Pilot subcarrier
Tal Pardo · Prof. Tirza Routtenberg and Prof. Nir Shlezinger
Notes: Welcome and thank you all for being here. Over the next 25 minutes I'll walk through the pilot placement problem, the model-based approach we've built, what the experiments taught us, where a prior learned CNN approach fell short, and a proposal for a deep RL agent to take this further.

## Slide 2: Agenda
01
Problem formulation
02
The model-based algorithm under a known prior
03
Main takeaways from experiments
04
CNN MSE predictor
05
Proposal: a deep reinforcement-learning pilot-placement agent

## Slide 3: Why pilot placement matters
SECTION 1 · PROBLEM FORMULATION
Pilots consume spectrum that could otherwise carry data — every pilot subcarrier is overhead, not payload.
Channel estimation accuracy depends on both how many pilots are used and where they are placed.
The standard baseline is fixed, uniformly-spaced pilots: simple, but blind to the actual channel.
This talk asks: can placement be adaptive — and eventually learned — to spend that overhead more efficiently?
Fixed, uniform pilot placement
Same spacing every time, regardless of the channel — wasteful when correlation structure means some subcarriers reveal far more than others.

## Slide 4: System model
MIMO-OFDM channel with antennas and subcarriers, vectorized column-by-subcarrier as .
Each step measures one new, not-yet-piloted subcarrier k:
That measurement is fed into a Bayesian (LMMSE) update, never remeasured again.
One step of measurement
Rows = antennas
Subcarrier k, measured this step

## Slide 5: Problem formulation
A sequential decision problem: which subcarrier to pilot next, repeated until a stopping rule is met.
Tx
Channel
LMMSE Channel estimator
posterior updates (ĥ, P)
Yes?
Output final channel estimate
Rx
Error estimator
Is small enough ?
No?
Active sampling:
Choose next pilot subcarrier

## Slide 6: LMMSE recap
SECTION 2 · MODEL-BASED ALGORITHM
Every new pilot measurement updates a Bayesian posterior belief — mean and covariance — over the whole channel.
is the full state the policy sees: a posterior mean and a posterior covariance over all N channel entries.
A key property
P depends only on which subcarriers have been measured thru and the assumed Σ thru — never on the realized data y. It is a belief, not a measurement.
After the first measurement is taken, we initiate the channel estimate and covariance:

## Slide 7: The active greedy policy
At every step, pick the unused subcarrier that maximizes a trace-minimization score:
In our settings antennas , subcarriers.
Interpretation
The trace term estimates how much piloting subcarrier k would shrink posterior uncertainty — a one-step-lookahead information-gain score.
The one assumption it needs
The true covariance Σ must be known exactly — P, and therefore J(k), is only as good as that prior.

## Slide 8: Baseline: active beats fixed, on Gaussian matched prior
Covariance created with Kronecker:
This is the best case for the greedy heuristic: the assumed Σ is exactly correct.

## Slide 9: Sampling the same subcarrier repeatedly
Covariance created with Kronecker:
Repeating the same subcarrier barely lowers the MSE: 0.704 → 0.702 from 2 to 32 pilots.
Only SC 15's noise averages out (σ²/m); the other subcarriers are learned only via correlation.

## Slide 10: Results on realistic TDL-A channels
SECTION 3 · WHAT THE EXPERIMENTS SHOW
Kronecker prior: active still beats fixed, but a true-vs-estimated gap opens — the model's confidence no longer matches reality.
Empirical prior (fit from TDL-A Monte Carlo draws) closes much of that gap.
Consistent with exp2: replacing a mismatched analytic prior with an empirical covariance estimate partially recovers active's advantage.
Source: new/experiments/exp3_true_vs_estimated_err.py · new/figures/exp1-6/exp3_tdl_err.png

## Slide 11: The gap
Main conclusions:
on a matched prior the active selection is better.
The oracle picks based on one lucky-or-unlucky realized noise draw per candidate, while active picks based on noise-independent expected information gain — so the oracle can occasionally get fooled by a lucky draw into picking a less informative subcarrier, while active never can.

## Slide 12: A learned 1-D CNN pilot allocator
SECTION 4 · THE LEGACY CNN APPROACH
CNN that predicts, for every candidate subcarrier, the error that piloting it would leave — then greedily picked the argmin.
CNN
Output
The most informative subcarrier
CNN
Pilot friction
1-D CNN along the subcarrier axis
Input
7 × 32
Conv1d
k = 5
Conv1d
k = 5
Conv1d
k = 3
Output
32
GroupNorm + GELU between layers, ending in 1×1 convolutions

## Slide 13: It outperformed every baseline tested
Final-step mean MSE, 250 Monte Carlo TDL-A channels:
Policy | Final MSE | vs. Active
CNN (ours) | 0.00163 | ≈1.6× better
Active | 0.00258 | —
Random | 0.00272 | —
Fixed | 0.00322 | —
Coherence | 0.00327 | —
Source: Final_Presentation - Gilead ans Tal.pptx (legacy old/ framework)

## Slide 14: But its gains were never stress-tested
Single scenario: only TDL-A fading tested — no prior-mismatch, non-Gaussian, low-rank or block-cluster stress tests like exp1–9.
Single SNR point — performance at other SNRs is unknown.
This motivates revisiting pilot placement with a method designed for cross-scenario robustness from the start.

## Slide 15: Optional datasets
Space-frequency
Time-frequency

## Slide 16: Neither baseline is enough: the active policy needs a prior it can't have, and the CNN was never tested for the robustness this project's own experiments say matters.
SECTION 5 · PROPOSAL
A deep RL agent can optimize the real, long-horizon placement objective end-to-end — without a hand-coded score or a proxy training target.

## Slide 17: MDP formulation
Agent
policy network
Action
pick an unused subcarrier (masked)
Environment
measures & updates state
Reward
Δ true NMSE (training only)
State — built only from Σ-free quantities
Pilots-used mask
|ĥ| magnitude (Σ-free estimate)
A model-free measurement residual
SNR · pilots-used fraction
Deliberately excluded
J(k) and the posterior block-trace both require an assumed Σ — exactly what deployment doesn't have. Getting ĥ and the residual from a Σ-free estimator (not today's LMMSE posterior) is an open implementation question.

## Slide 18: Open research questions
Training data: which channels?
Key properties to have:
Structure to learn.
Smoothness.
Important to remember: If every subcarrier is equally informative, the active-vs-fixed gap vanishes and there is nothing to learn from.
Prior free design: how to update a wrong initial prior?
The agents indirectly learns the prior – how to change the covariance along the way?
Model-based solutions.

## Slide 19: Training design
Scenario registry
versioned, checked-in config
Simulator (new/)
live environment, not a fixed log
Rollout buffer
cached episodes, for sweeps & reuse
Policy update
MaskablePPO
Repeats across sweeps — the same versioned scenario spec feeds every run, so results are comparable.
Online rollouts against the live simulator — the agent is never capped by a logged heuristic's coverage.
Exact mismatched-prior parameterization is explicitly deferred to a later pass.

## Slide 20: Algorithm & infrastructure
MaskablePPO
sb3-contrib
The action space shrinks every step — pick an unused subcarrier. MaskablePPO handles that natively, instead of hand-rolling action masking on top of a custom policy gradient.
ClearML
experiment tracking
Tracks metrics and configs across scenario sweeps, versions cached rollouts, and orchestrates hyperparameter sweeps — the reproducibility layer this repo doesn't have yet.

## Slide 21: Evaluation plan
The trained policy wraps the existing PilotPolicy protocol, dropping directly into run_until_threshold for an apples-to-apples comparison across every exp1–9 scenario family.
Fixed
uniform, blind
Active
greedy, needs known Σ
Legacy CNN
one scenario only
RL agent
to be measured
Oracle
upper bound (slide 10)
Increasing information used, left to right — the open question is how close the RL agent lands to the oracle without ever seeing Σ.

## Slide 22: Thank you.
Questions?
Notes: Happy to go deeper on any of the open questions: the mismatched-prior parameterization, the sigma-free observation design, or the channel screening procedure.